# OpenHumidor Wireless Protocol
V4:
Operation

Sensor:

0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17
0xCA	0x55	Module Address					Device flags	Error / flags	Temperature		Humidity		Supply Voltage		Signal quality	Message ID

Base:

0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17
0xCA	0x55	Device flags	Humidifier	Fan	Fire Again		Message ID		0xFF	0xFF	0xFF	0xFF	0xFF	0xFF	0xFF	0xFF	0xFF

Errorflags:
7	6	5	4	3	2	1	0
DHT_TOO_QUICK	DHT_CHECKSUM	DHT_DATA_TIMEOUT	DHT_SYNC_TIMEOUT	DHT_ACK_TOO_LONG	DHT_NOT_PRESENT	DHT_BUS_HUNG	RECEIVED_NOTHING

Init

Sensor:
0	1	2	3	4	5	6	7	8	9

0-1: InitHeader (0xCA | 0x55)
2-6: Module Raddress
7: Suggested ID (from EEPROM)
8: Reserved (0xFF)
9: Checksum

Base:

0	1	2	3	4	5	6	7	8	9

0-1: InitHeader (0xCA | 0x55)
2: ModuleID (0-255)
3-8: Reserved (0xFF)
9: Checksum

Operation

Sensor:

0	1	2	3	4	5	6	7	8	9

0-1: DataHeader (0x44 | 0x32)
2: ModuleID
3: DeviceFlags (Humidifier, Hygro, Fan)
4: Errorflags
5-6: Temperature
7-8: Humidity
9: Checksum

Base:

0	1	2	3	4	5	6	7	8	9

0-1: DataHeader (0x44 | 0x32)
2: ModuleID
3: DeviceFlags
4: Switch Humidifier (0-255)
5: Switch Fan (0 | 255)
6-7: Fire again in X centiseconds
8: Reserved (0xFF)
9: Checksum

The checksum consists of all bytes added up and truncated to the LSB: (b1 + b2 + b3 + b4 … ) & 0xFF